## Slide 1: LogicFusion’s Hands-on Robotics EV3 Level 2!
Welcome to

## Slide 2: Orientation Agenda
General class rules
8 weeks summary
Evaluations
LogicFusion Website

## Slide 3: Introductions
Tell us something about you!
  What is your name?
  Which school are you from?
  What grade are you in?
  Why are you taking this course?
  What’s your favourite thing about robotics so far?
  One unique fact!

## Slide 4: General Class Rules
Respect
Talking
Asking Questions
Participation
Absences
Working with Lego

## Slide 5: Respect
Respect the instructor
  Do what’s being asked
Respect fellow classmates
  Encourage each other
  Give everyone a chance to participate
  No putdowns
Make the classroom safe and inclusive! 

## Slide 6: Talking
Please pay attention when the instructor is speaking
  Stop what you are doing and listen attentively
  Turn off the monitor
  Don’t speak when someone else is speaking
Remember, when you are talking, everyone else listens!

## Slide 7: Asking Questions
Please raise your hand
Wait until you are picked
Don’t interrupt others
Ask your questions after class (or during free work time) when:
  Your question takes long to answer
  You have many questions
  Your question is unrelated to what is being taught

## Slide 8: Participation
Please raise your hand
Wait until you are picked
Don’t shout out your answer
Participation is strongly encouraged!

## Slide 9: Absences
Let the instructor know one class before you are going to be absent
  If it is an unexpected absence, let the instructor know as soon as possible

## Slide 10: Working with the Lego
Keep your workspace clean
Be careful with the pieces
Don’t force any of the pieces in
Ask if you aren’t sure
Pick up any dropped pieces
Tidy up the box like how you found it
Have fun!

## Slide 11: 8 Weeks Summary
Logistics, Interface, Motors, & Base Car
Wait, Loops, & Top Spinner
Sound Block & Sensors
Colour Sensor & Switches
Buffalo Bumper Car & Door Alarm
My Block & Mini Rover
Mini Golf & Challenge
Final Project: Design a Robot!
Notes: Week 1: Interface, Motors, Base Car
Week 2: Wait, Loop, Top Spinner
Week 3: Sound Block, Sensors
Week 4: Colour Sensor, Switches
Week 5: Buffalo Bumper Car, Door Alarm
Week 6: My Block, Mini Rover
Week 7: Mini Golf, Challenge
Week 8: Design a Robot

## Slide 12: Evaluations – Grading
You will be graded on the final project
You must obtain 60% or above in order to achieve a certificate or course badge

## Slide 13: LogicFusion Account
http://www.logicfusion.ca/users/signup
Please sign up for an account! (Add the course if you were a previous student)
Sign up code: LogicFusionSignup789
Your certificate will be printed based on the first and last name of your account, so PLEASE USE YOUR REAL NAME!
Notes: INSTRUCTORS PLEASE VERIFY THAT ALL STUDENTS HAVE ACHIEVED THE EV3 BADGE.
INSTRUCTORS PLEASE DO NOT SKIP THIS. If you don’t have access to wifi, use the sign up program!

## Slide 14: An Introduction
Hands-on Robotics EV3 Level 2, Week 1

## Slide 15: Motors
Notes: This is a motor. It’s like the motors in our cars that make the wheels turn.
This motor can measure exact distance and speed.
What do motors do?
Takes electric signals and transforms it into a form of motion
Unlike sensors which are input which takes information in, motors are output which produce some output. They act like printers or monitors for our computer.
Image Source: http://cache.lego.com/e/dynamic/is/image/LEGO/45502?$main$

## Slide 16: Sensors
Notes: These are sensors. Touch, Ultrasonic, Light, Gyroscope
Sensors are used to give inputs to the robot, different from the motors being outputs.
Image Source: http://www.ucalgary.ca/IOSTEM/files/IOSTEM/media_crop/44/public/sensors.jpg

## Slide 17: EV3 Brick
Notes: This is the brain of the robot.
The inputs plug into the numbers.
The outputs plug into the letters.
Image Source: http://cache.lego.com/r/education/-/media/lego%20education/home/images/products/mindstorms%20ev3/45500_713x380_mainproduct.png?l.r=1276236109

## Slide 18: Build the Base Car
Follow the instructions in the Hands-on Robotics EV3 2 Project Instructions pdf

## Slide 19: EV3 Software
Notes: Click the plus sign to start a new project

## Slide 20: One Motor
Large Motor Block

## Slide 21: The Canvas
Notes: Double click the name that appears on the project tab to rename the project

## Slide 22: Large Motor
Notes: What do we want our base car to do? We want it to move forward.
Let’s take a look at the 2nd block in the Action (green) category.

## Slide 23: Large Motor
Notes: Here we see a couple of things on the Large Motor block.
What do you think these are?
Answer: (From left to right) How to measure duration (infinite, time, rotations) , power, duration and next action. At the top right, there is also a selection for which port the motor is plugged into.

## Slide 24: Two Motors
Move Steering Block

## Slide 25: Move Steering
Notes: Since we have two motors on our robot, we will use Move Steering. Click on the third button in the Action category, which is the move steering command, and drag it onto the start.
Why do you think we use this block instead of the Large Motor block?
Answer: Move Steering moves both motors at the same time.

## Slide 26: Move Steering
Notes: Let’s take a closer look at the Move Steering block.
As we can see, the block looks very similar, we have the same settings such as how to measure duration, power, duration and next action.
The things we know that are different are steering and the motors selected. The steering setting allows us to choose which way the robot will go, turn left, turn right, go straight or spin on the spot. The motors selected right now show B + C because we have to select two motors. Think of B motor as the left motor and C motor as the right motor and when you use the slider for the steering setting, moving the slider left means turn towards motor B (left side) and moving the slider right means turn towards motor C (right side).

## Slide 27: Activity 1
Make a program that will make the Base Car go forward for 2 seconds
Solution

## Slide 28: Activity 2
Make a program that will make the Base Car go forward for 2 seconds, then go backwards for 2 seconds
Solution
Notes: The power needs to be changed to negative for the car to move backwards direction.

## Slide 29: Activity 3
Make a program that will make the Base Car go forward for 2 seconds, turn around 180 degrees, then go forward for 2 seconds
Possible Solution:
Notes: Answers may vary.
Common mistake: degrees set to 180 rotation – this is how much the motor turns, not how much the base car turns. Need to try out different values and test it out to see.
At this point, you can teach students how to connect and download onto their brick.

## Slide 30: Activity 4
Make a program that will make the Base Car go in a square
Notes: If there is time, continue with these challenges.
Solutions are trial and error.

## Slide 31: Activity 5
Make a program that will make the Base Car go in a triangle
Notes: If there is time, continue with these challenges.
Solutions are trial and error.

## Slide 32: Activity 6
Make a program that will make the Base Car go in a pentagon
Notes: If there is time, continue with these challenges.
Solutions are trial and error.

## Slide 33: Activity 7
Make a program that will make the Base Car go in a hexagon
Notes: If there is time, continue with these challenges.
Solutions are trial and error.

## Slide 34: Activity 8
Make a program that will make the Base Car go in an octagon
Notes: If there is time, continue with these challenges.
Solutions are trial and error.

## Slide 35: Waits & Loops
Hands-on Robotics EV3 Level 2, Week 2

## Slide 36: Review
Move Steering Block
  Select Port
  Choose Direction
  Set Power
  Set Duration
  Brake at End

## Slide 37: Wait
Wait Block

## Slide 38: Wait
Notes: Wait for a certain amount of time. Robot does nothing while it’s waiting
Other functions include waiting for some input from sensors.

## Slide 39: Wait

## Slide 40: Wait
Wait Block
  Wait for something
  Time
  Sensor (Next Week)
Notes: Wait block pauses the program

## Slide 41: Top Spinner
Build the Top Spinner from the Hands-on Robotics EV3 2 Project Instructions pdf
Make the following program for the Top Spinner
  The program does nothing until the middle button is pressed
  When the middle button is pressed, spin the motor for 5 seconds

## Slide 42: Top Spinner Program Solution

## Slide 43: Loop
Loop Block

## Slide 44: Loop
Loop Block
  Repeat something
  Unlimited
  Count
  Time
  Sensors (Next Week)
Notes: Can loop until a duration of time, number of times, or until a condition is met (true).
Can also loop unlimited.

## Slide 45: Top Spinner
Make the following programs for your Top Spinner
  A motor that keeps spinning, using a loop
  A motor that keeps spinning, without a loop
Notes: Without a loop, need to put a wait block at the end (doesn’t matter the settings, as long as not time). If not, the program will end right away.

## Slide 46: Top Spinner Solution (with a loop)
Notes: Need solution without a loop

## Slide 47: Top Spinner Solution (without a loop)
Notes: Without a loop, need to put a wait block at the end (doesn’t matter the settings, as long as not time). If not, the program will end right away.

## Slide 48: Sound Block & Sensors
Hands-on Robotics EV3 Level 2, Week 3

## Slide 49: Review
Wait Block
  Wait for sensor
  Wait for time
Loop Block
  Repeat things

## Slide 50: Sound
Sound Block

## Slide 51: Sound Block

## Slide 52: Sound Block
Notes: File is just any file
Tones are different sounding beeps
Notes are musical notes
Volume.
Play until completion

## Slide 53: BeatBox
Create a program that uses the tones/notes to play a song or a beat
You do not need to build anything for this activity
Notes: Sample solution needed

## Slide 54: BeatBox Sample Solution

## Slide 55: Sensors
Using Sensors

## Slide 56: Sensors – Brick Buttons
Notes: Can be used in wait block as well as loop.

## Slide 57: Sensors – Brick Buttons

## Slide 58: Sound Board
Create a program that uses the buttons on the brick to play different sounds/notes/tones
Each of these buttons should play a different note:
  Left button
  Middle button
  Right button

## Slide 59: Sound Board Sample Solution
Notes: Buttons need to be pressed in the right order for this to work.

## Slide 60: Sensors – Touch Sensor
Notes: Also works with wait and loop blocks

## Slide 61: Sensors – Touch Sensor

## Slide 62: Button Controlled Motor
Attach a touch sensor and a motor to the Brick
Create a program that will turn the motors when the touch sensor is pressed

## Slide 63: Button Controlled Motor Solution

## Slide 64: Sensors - Ultrasonic
Notes: Instead of true or false, you have a comparison (e.g. closer/farther distance)

## Slide 65: Sensors - Ultrasonic

## Slide 66: Colour Sensor & Switches
Hands-on Robotics EV3 Level 2, Week 4

## Slide 67: Review
Sound Block
  Play a Note
  Play a Tone
  Play a File
Sensors
  Button
  Touch
  Ultrasonic
Notes: Gyro sensor?

## Slide 68: Colour
Colour Sensor

## Slide 69: Sensors – Colour Sensor

## Slide 70: Sensors – Colour Sensor

## Slide 71: Switches
If Statements

## Slide 72: Switches

## Slide 73: Switches
Notes: Use compare for switches to compare the value with a value you want to test.

## Slide 74: Colour Scanner
Build the Colour Scanner from the Hands-on Robotics EV3 2 Project Instructions pdf
Program the Colour Scanner to do the following:
  Detect blue
  Play a sound
  Keep running until you stop the program

## Slide 75: Colour Scanner Solution

## Slide 76: Buffalo Bumper Car & Door Alarm
Hands-on Robotics EV3 Level 2, Week 5

## Slide 77: Review
Colour Sensor
  Scan for colour
Switches
  Used to make decisions in programming

## Slide 78: Buffalo Bumper Car
Build the Buffalo Bumper Car from the Hands-on Robotics EV3 2 Project Instructions pdf
Program the Bumper Car to do the following:
  Detect hitting something
  Backup and turn
  Go forward if not hitting something

## Slide 79: Buffalo Bumper Car Solution

## Slide 80: Door Alarm
Build a Door Alarm
  Secure the Ultrasonic Sensor to the Brick
  Plug the Ultrasonic Sensor into Port 4
Program the Door Alarm so that it does the following:
  Detect when someone gets closer than 30 cm
  Play any sound/tone/note 3 times when detected

## Slide 81: Door Alarm Solution

## Slide 82: My Block & Mini Rover
Hands-on Robotics EV3 Level 2, Week 6

## Slide 83: Review
Buffalo Bumper Car
  Switches
  Loop
Door Alarm
  Loop
  Switch

## Slide 84: My Block
My Block

## Slide 85: My Block
Custom Block
  Can add other blocks
  Useful for long tasks

## Slide 86: My Block
Notes: What is My Block
Highlight the blocks you want in the My Block

## Slide 87: My Block

## Slide 88: My Block

## Slide 89: My Block

## Slide 90: Mini Rover
Build the Mini Rover from the Hands-on Robotics EV3 2 Project Instructions pdf
Program the Mini Rover
  Control the rover using the Brick
  Left button turns left
  Middle button goes straight
  Right button turns right

## Slide 91: Mini Rover Solution

## Slide 92: Mini Golf & Challenge
Hands-on Robotics EV3 Level 2, Week 7

## Slide 93: Review
My Block
Mini Rover
  Switch

## Slide 94: Mini Golf
Build the Mini Golf from the Hands-on Robotics EV3 2 Project Instructions pdf
Program the Mini Golf
  Left button swings soft
  Middle button swings medium
  Right button swings hard

## Slide 95: Mini Golf Solution

## Slide 96: Challenge!
Choose one of the projects we have done before from the Hands-on Robotics EV3 2 Project Instructions pdf
Create a My Block to use in the program
  Feel free to add sounds, display, or your own personal touch to the programs

## Slide 97: Final Project
Hands-on Robotics EV3 Level 2, Week 8

## Slide 98: Final Project – Design a Robot
Design your very own robot
  Plan how you want it to look
  Build the robot
  Make sure to include sensors and motors to the program
  Be creative!
Program the robot
  Use at least 7 blocks
Notes: Image Source: http://www.erichuang.com/uploads/1/4/8/2/14828090/652998426_orig.png?294
Out of 10
7 blocks
At least 1 sensor
At least 1 motor
Creativity